## Slide 1: COMP90050:Advanced Database Systems Professor Rao Kotagiri Lecture Set6

## Slide 2: TPC
Aims of TPC (Transaction Processing Council)
Create good benchmarks
  Good benchmarks are like good laws. They lay the foundation for civilized (fair) competition.
  No matter how clear-cut the rules appear to be when the benchmark specifications are written, there are always grey areas, and loopholes left in the benchmark law. Classic examples are many loop holes in Taxation Laws.
  There must be a way of addressing and resolving these grey areas and loopholes in a fair manner.
Take the role to see the reported benchmarks are valid.
  Creating a good process for reviewing and monitoring those benchmarks.

## Slide 3: The State Of Nature
End-user business transactions (online transaction processing, OLTP) began to appear in the early 1980's.
  The first application that received wide-spread focus was automated teller transactions (ATM),
  ATM trend ripple through almost every area of business, from grocery stores to gas (petrol) stations.
As opposed to the batch-computing model that dominated the industry in the 1960's and 1970's, this new online model of computing had
  Relatively unsophisticated clerks and consumers directly conducting simple update transactions against an on-line database system. Almost all transactions are now performed online – from grocery shops, banks to government organisations
  On-line transaction processing (OLTP) industry now represents several billions of dollars in annual sales.

## Slide 4
Given the size of this market the race--over who could claim the best OLTP system began and the competition among computer vendors was intense.
But, how to prove who was the best?
  Benchmarking
  It was through Omri's initiative and leadership that the TPC was founded 1980.
During mid-1980's, computer system and database vendors began to make performance claims based upon the TP1 benchmark, a benchmark originally developed within IBM that then found its way into the public domain.
TP1 measured the performance of a system handling ATM (Auto Teller Machines) transactions in a batch mode without the network or user interaction components of the system workload (similar in design to what later turned out to be TPC-B).

## Slide 5
The TP1 benchmark had two major flaws.
  First, by ignoring the network and user interaction components of an OLTP workload it gave inflated performance numbers.
  Secondly, the benchmark was poorly defined and there was no supervision or control of the benchmark process.
As a result, the TP1 marketing claims had little credibility .
The situation also deeply frustrated vendors who felt that their competitors' marketing claims were based upon flawed benchmarks.

## Slide 6: Early Attempts at Civilized Competition
In the April 1, 1985 issue of Datamation, Jim Gray in collaboration with 24 others from academy and industry, published (anonymously) an article titled, "A Measure of Transaction Processing Power."
This article outlined a test for on-line transaction processing which was given the title of "DebitCredit."
Unlike the TP1 benchmark, Gray's DebitCredit benchmark specified a true system-level benchmark where the network and user interaction components of the workload were included.

## Slide 7: Early Attempts at Civilized Competition …
In addition, it outlined several other key features of the benchmarking process that were later incorporated into the TPC process:
  Total system cost published with the performance rating.
  Total system cost included all hardware and software used to successfully run the benchmark, including 5 years maintenance costs.
Until this concept became law in the TPC process, vendors often quote only part of the overall system cost that generated a given performance rating.
Benchmark was specified in terms of high-level functional requirements rather than specifying any given hardware or software platform or code-level requirements.
This allowed any company to run this benchmark if they could meet the functional requirements of the benchmark.

## Slide 8: Early Attempts at Civilized Competition …
The benchmark workload scale up rules:
  the number of users and size of the database tables increased proportionally with the increasing power of the system to produce higher transaction rates.
The scaling prevented the workload from being overwhelmed by the rapidly increasing power of OLTP systems.
The overall transaction rate would be constrained by a response time requirement.
In DebitCredit, 95 percent of all transactions had to be completed in less than 1 second.
The TPC lays Down the Law.

## Slide 9: Early Attempts at Civilized Competition …
Gray's DebitCredit ideas were widely praised by industry opinion makers, the DebitCredit benchmark could not stop bad benchmarking.
Without a standards body to supervise the testing and publishing, vendors began to publish extraordinary marketing claims on both TP1 and DebitCredit.
They often deleted key requirements in DebitCredit to improve their performance results.

## Slide 10: Early Attempts at Civilized Competition …
From 1985 through 1988, vendors used TP1 and DebitCredit--or their own interpretation of these benchmarks.
On August 10, 1988, Serlin had successfully convinced eight companies to form the Transaction Processing Performance Council (TPC).

## Slide 11: TPC-A
Using the model around the DebitCredit benchmark, the TPC published its first benchmark, TPC Benchmark A (TPC-A) within one year (November 1989).
TPC-A differed from DebitCredit in the following respects:
  The requirement that 95 percent of all transactions must complete in less than 1 second was altered to 90 percent of transactions must complete in less than 2 seconds.
  The number of emulated terminals interacting was reduced to a requirement of 10 terminals per tps and the cost of the terminals was included in the system price.

## Slide 12
  TPC-A could be run in a local or wide-area network configuration (DebitCredit has specified only WANs).
  The production-oriented requirements of the benchmark were strengthened to prevent the reporting of peak, unsustainable performance ratings.
  Specifically, the ACID requirements were imposed and specific tests added to ensure ACID viability.
  Finally, TPC-A specified that all benchmark testing data should be publicly disclosed in a Full Disclosure Report.
The first TPC-A results were announced in July 1990. Four years later, at the peak of its popularity, 33 companies published on TPC benchmarks and 115 different systems had published TPC-A results. In total, about 300 TPC-A benchmark results were published.

## Slide 13: Early Attempts at Civilized Competition …
  The first TPC-A result was 33 tpsA at a cost of $25,500 per transaction or tpsA (Total cost in excess of $8.4M in 1990). The highest TPC-A result ever recorded was 3,692 tpsA with a cost of $4,873 per tpsA (Cost of $18M in 1990!)
The increase was 111 times but the increase in tpsA ratings is just too great. The increase can be due to:
  the first benchmark test is usually run for bragging rights and is grossly unoptimized compared to later results;
  real performance increases of hardware and software products;
  vendors improving their products to eliminate performance bugs exposed by the benchmark,

## Slide 14: Early Attempts at Civilized Competition …
  vendors playing the benchmarking game effectively--learning from each other on how best to run the benchmark.
Achievement of TPC-A that for the first time, it provided the industry with an objective and standard means of comparing the performance of a vast number of systems.

## Slide 15: TPC-B
TPC-A's principal strengths was that it was an end-to-end system benchmark that exercised all aspects of an OLTP system.
TP1 (and later TPC-B) was the batch version of DebitCredit, without the network and user interaction (terminals)
A strong block of companies within the TPC, including hardware companies who sold "servers" and database software companies, felt that the TPC-B model was more representative of the customer environments they sold into.
Opposition TPC-B is that the tps rates would be artificially high, the total system cost since the network and terminal pricing would be eliminated would be artificially low, thereby artificially boosting TPC-B's price/performance ratings.
But TPC-B proponents eventually won the day and in August 1990, TPC-B was published as the second TPC benchmark standard.

## Slide 16
The first TPC-B results were published in mid-1991 and by June 1994, at the peak of its popularity, TPC-B results had been published on 73 systems.
In total, about 130 TPC-B tests were published.
In all, there were about 2.5 times more TPC-A results published.
The first TPC-B result was 102.94 tpsB with a cost of $4,167 per tpsB (Cost. $420K)
The highest TPC-B rating was a 2,025 tpsB result, and the best price/performance number was $254 per tpsB. (Cost of $514K)
In summary, the top TPC-B ratings increased by a factor of 19 and the price performance rating improved by a factor of 16.
In January 1998, the TPC announced the formation of a Web Commerce benchmark (TPC-W) which measured OLTP and browsing performance only of the web server, excluding the network and human interaction components of the overall system.

## Slide 17
1980: TP1: just debit credit– no network or computing cost included
1985: DebitCredit: debit credit– with network, computing and maintenance cost included with 95%completions within 1 sec time
1988: TPC-A: Debitcredit– with network, computing and maintenance cost included with 90%completions with in 2 secs time
1990: TPC-B: debit credit– with no network costs for benchmarking servers
1998: TPC-W: Web Commerce benchmark measured OLTP and browsing performance only of the web server, excluding the network and human interaction

## Slide 18: Political Reform Begins Immediately
As soon as vendors began to publish TPC results, complaints from rival vendors began to surface.
Every TPC result had to be accompanied by a Full Disclosure Report (FDR).
But, what happens when people reviewed the FDR and didn't like what they read?
How could protest be registered and how would it be adjudicated?
It became apparent to the Council that without an active process for reviewing and challenging benchmark compliance, there was no way that the TPC could guarantee the level playing field that the TPC had promised the industry.
Throughout 1990 and 1991, the TPC embarked on a political journey to fix this hole in its process.

## Slide 19: Technical Advisory Board
The Technical Advisory Board (TAB), constituted as just an advisory board, became the arm of the TPC where the public or companies could challenge published TPC benchmarks.
The TAB process, which remains in place today, established a fair, deliberative mechanism for reviewing benchmark compliance challenges. Once the TAB has thoroughly researched and reviewed a challenge, the TAB makes a recommendation to the full Council.
The full Council then hears the TAB's report, discusses and debates the challenge, and then votes on the challenge.
If the Council finds the result non-compliant in a significant or major way, the result is immediately removed as an official TPC result.

## Slide 20: Benchmarking Versus Benchmarketing
By the spring of 1991, the TPC was clearly a success. Dozens of companies were running multiple TPC-A and TPC-B results.
Not surprisingly, these companies wanted to capitalize on the TPC's cachet and leverage the investment they had made in TPC benchmarking.
Several companies launched aggressive advertising and public relations campaigns based around their TPC results.
In many ways, this was exactly why the TPC was created: to provide objective measures of performance.
What was wrong, therefore, with companies wanting to brag about their good results?
What was wrong is that there was often a large gap between the objective benchmark results and their benchmark marketing claims--this gap, over the years, has been dubbed "benchmarketing."

## Slide 21
  TPC was faced with an ironic situation.
  It had poured an enormous amount of time and energy into creating good benchmark and even a good benchmark review process.
  The TPC had no means to control how those results were used once they were approved. Out of these Council debates emerged the TPC's Fair Use policies adopted in June, 1991.
  When TPC results are used in publicity, the use is expected to adhere to basic standards of fidelity, candor, and due diligence,
  The qualities that together add up to, and define, Fair Use of TPC Results.
  Fidelity: Adherence to facts; accuracy
  Candor: Above-board; needful completeness
  Due Diligence: Care for integrity of TPC results

## Slide 22
  This issue has two sides.
  On the one hand, companies spend hundreds of thousands of dollars, even millions of dollars, running TPC benchmarks to demonstrate objective performance results.
  It's quite legitimate, therefore, for these companies to market the results of these tests and compare them with the results of their competitors.
  On the other hand, no company has a right to misrepresent or mislead the public, regardless of how legitimate the benchmark tests may be.
  So where does the "war" on benchmarketing stand?
  In April, 1993 the Standish Group, a Massachusetts-based consulting firm, charged Oracle that it had added a special option (discrete transactions) to its database software, with the sole purpose of inflating Oracle's TPC-A results.

## Slide 23
May 17, 1993 issue of Network World were not uncommon, "Report Finds Oracle TPC results to be misleading; says option discredits TPC-A as benchmark."
New Anti-Benchmark Special Prohibition
  September, 1993, the TPC passed Clause 0.2, which contains the sweeping prohibition against benchmark specials that become a bedrock of the TPC process to ensure, relevant benchmarks
Clause 0.2 in TPC-A and TPC-B went into effect in June, 1994. Oracle decided not to test its discrete transaction option against the new anti-benchmark special rules in the specifications and withdrew all of its results by October, 1994

## Slide 24: New TPC Auditing Process
As a result of the 1993 controversies, the TPC realized that the millions of dollars being invested in the running of TPC benchmarks would be completely wasted if the credibility of the results were challenged.
The result of this, TPC in September and December, 1993, created a group of TPC certified auditors who would review and approve every TPC benchmark test and result before it was even submitted to the TPC as an official benchmark or publicized.
While TPC benchmarks are still reviewed and challenged on a regular basis, the TPC auditing system has been very effective in preventing most of the bad benchmarking.

## Slide 25: New and Better Benchmarks
Two benchmark activities were launched in 1990, the development of TPC-C, the next generation OLTP benchmark, and TPC-D, a decision support benchmark.
Both TPC-C, which was approved as a new benchmark in July, 1992 and TPC-D, which was approved in April, 1994.
The first TPC-C result published in September, 1992 was 54 tpmC result with a cost per tpmC of $188,562 (cost $10M)
More than six years later, the top result is a 52,871 tpmC with a cost per tpmC of $135 (cost 0f $7M) with performance improvement 1578.3 times taking into consideration of inflation of 13% over 6 years.

## Slide 26
The first TPC-D result was a 100 GB result in December, 1995 with a throughput performance rating of 84 QthD (Query throughput for D) and a price/performance rating of $52,170 QphD. (In 2000, the top 100 GB throughput result that has been produced is 1205 QthD and $1877 QphD.
Currently, there are 28 official TPC-D results.

## Slide 27: Aborted Benchmark Efforts
TPC Server Benchmark (TPC-S)
  a server version of TPC-C (as opposed to TPC's end-to-end system model) that would be both easier and less expensive to run.
TPC-E, the "Enterprise" Benchmark
  TPC-C was significantly more complex and robust than earlier TPC-A benchmark, but it still wasn't complex enough to stress very large, enterprise-class systems. TPC-E would demand that systems provide faster response times, higher I/O bandwidth, and concurrent batch processing, as well as fast recovery times which are not required of smaller systems.

## Slide 28: Aborted Benchmark Efforts
TPC Client/Server
  TPC-C/S was designed to model the more complex client/server environment with a wider range of applications and data.
  Three new transactions were to be added to TPC-C, including an order analysis, market analysis and an image transaction.

## Slide 29
Company | System | tpmC | Price/tpmC USD | Time result reported | Total Cost of the Systemin US$s
Oracle | SPARC T5-8 Server | 8,552,523 | 0.55 | 09/25/13 | $4.7M
IBM | IBM System x3850 X5 | 3,014,684 | 0.59 | 09/22/11 | $1.78M
Oracle | Sun Server X2-8 | 5,055,888 | 0.89 | 07/10/12 | $4.5M
Oracle | SPARC SuperCluster with T3-4 Servers | 30,249,688 | 1.01 | 06/01/11 | $30.2M
IBM | IBM Power 780 Server Model 9179-MHB | 10,366,254 | 1.38 | 10/13/10 | $14.3M
Oracle | Sun SPARC Enterprise T5440 Server Cluster | 7,646,486 | 2.36 | 03/19/10 | $18.0M

## Slide 30
The TPC's Newest Benchmark: TPC-W
  The TPC announced in 1998 a new Web Commerce Benchmark, called TPC-W.
  TPC-W is designed to represent a business (retail store, software distribution, airline reservation, etc.) that markets and sells a product or service over the Internet.
  The benchmark will measure the performance of systems supporting users browsing and processing orders on a business web site.
  TPC-W does not include user interaction aspects in its workload.